VHDL Cheat sheet

Applications of HDL
- Automated synthesis
- Design reuse
- functional validation and timing behaviour sims
- prototyping and design specification

Objectives of HDL
- Minimise design errors
- minimise design cost and time

	Behavior	Structure	Geometry
Architecture	System specs	System partitioning	floorplan
Register Transfer	algorithms	Module netlist (Muxs, registers)	Macro cells (IP blocks)
Logic	Boolean eqns	Gate netlist (gates, FFs)	Standard and lib cells
Circuit	Differential eqns	Transistor netlist	Mask and polys

Describes our model

VHDL → Simulation → Synthesis → Implementation

Behaviour	Syntax		Translation
Structure	Testbench	Gate/RTL netlist	Map – modules are mapped to resources
Dataflow	Logical verification and waveforms - timing		P & R

entity xorop is
Generic(
constant BIT_WIDTH: integer := 16);
    Port (
I1 : in STD_LOGIC_VECTOR(BIT_WIDTH - 1 downto 0);
I2 : in STD_LOGIC_VECTOR(BIT_WIDTH - 1 downto 0);
O : out STD_LOGIC_VECTOR(BIT_WIDTH - 1 downto 0));
end xorop;

architecture Behavioral of xorop is

begin
XR: process (I1,I2)
begin
O <= I1 XOR I2;
end process XR;

end Behavioral;

All Processes in VHDL are executed concurrently
- But within the process the instructions are executed sequencially
- variables can only be used within a process
Process must have
- either a sensitivity list or wait statement
- if there is a wait statement, its not synthesisable

VHDL Structure
Entity describes
external view of circuit
Architecture
- realises the entity
- provides an internal view of the circuit
- multiple architectures can exist in one entity
Modelling of archs
- Behavioral models
  - describe the behavior of the models
    - Algorithmic models
    - Dataflow models
- Structural models
  - Combines different modules with signals

variables use
“:=” for assignment

after (inertial or transport delay)
wait
wait for TIME
wait on CLK, ENABLE
wait until CONDITION
with sel select
Z <=	X(0) after 5ns when “00”;
X(1) after 5ns when “01”;
for K in X’range loop
if X(k) = ‘0’ then
Y <= ‘1’ after PD;
end if;
end loop;

case sel is
when “00” =>
state <= ‘1’;
D <=	"1111" when EN='0' else
"0111" when A='0' and B='0' else
"1011" when A='0' and B='1' else
"1101" when A='1' and B='0' else
"1110" when A='1' and B='1' else
"1111";

sll
shift left logical
(fill value is ‘0’)
srl
shift right logical
(fill value is ‘0’)
sla
shift left arithmetic
(fill value is right-hand bit)
sra
shift right arithmetic (fill value is left-hand bit)
rol rotate left
ror rotate right

examples:
“1100” sll 1 yields “1000”
“1100” srl 2 yields “0011”
“1100” sla 1 yields “1000”
“1100” sra 2 yields “1111”
“1100” rol 1 yields “1001”
“1100” ror 2 yields “00

...

arch abc of entity_name is

component mux2to1 is
port (
A,B in bit := ‘0’;
O out bit :=’0’;
);
end component;
signals

begin
end abc

Loops in circuits can be used as ring oscillators

Gated Clocks
- Energy efficiency
- Optimize the skew in clock distribution
- By accident!

Synthesis
Translation
Mapping
Place & Route